## Slide 1
Medical Laboratories
Flexible scopes of accreditation
June 2023

## Slide 2: What do we mean by ‘Scope’?
The official and detailed statement of activities for which an accredited conformity assessment body is granted accreditation
Documented in the Schedule of Accreditation published at www.ukas.com
For testing / medical laboratories identifies for each activity:
  Sample type(s)
  Component, parameter or characteristic tested
  Test or type of test performed and, as appropriate, the techniques, methods and/or equipment used
  Location(s) where the testing is carried out
  Issue date which allows traceability to when accreditation was granted for the activities

## Slide 3: Why a Flexible scope?
Is a fixed scope suitable for your service?
If things rarely change then probably yes
If many findings are raised at ETS assessments, definitely
But….
Change can be a constant
Need to implement new tests in short timeframes
Repeated cycles of Extension to Scope (ETS) application, assessment & grant with few or no findings
A lot of work (for UKAS as well)
Cost of multiple ETS

## Slide 4: UKAS process
A flexible scope must be applied for, assessed, and granted
AC6 application form
Other documents to be submitted with the application include documentation pertaining to the management & operation of flexible scopes, plus example(s) of implementation
Pre- and Post-assessment processes generally follow that of other ETS
Assessment includes the additional competencies needed to manage a flexible scope

## Slide 5: UKAS process
Extension to Scope / Initial Assessment
Onsite assessment
Surveillance / Reassessment
Assessment plan will include flexible scope management EVERY year
Additional assessment effort will be required throughout the 4-year cycle
Representative examples of inclusion of new tests within the flexible scope
  Accredited services are required to inform UKAS periodically of activities within the flexible scope (additions / removals)
  Frequency / format agreed & confirmed at initial grant

## Slide 6: What flexibility can be granted (GEN 4 UKAS Policy)?
(a) parameters, materials, sample types
(b) range of activity, tests/examinations
(c) methods, procedures, parameters, equipment, measurement, extent of technical/clinical area, specification
(d) type of activities undertaken at a location

## Slide 7: What flexibility can’t be granted (GEN 4 UKAS Policy)?
4.3 UKAS does not consider that the flexible scope approach is appropriate for allowing services to introduce a new activity where it has not previously demonstrated competence for undertaking the key components involved. An example of a new activity for testing/calibration would be a new analytical technique

## Slide 8: Boundaries
Boundaries to the flexibility must be clearly defined in the AC6, assessment, initial recommendation and then on the Schedule
Competencies must be demonstrated for all processes within these boundaries
Broad definitions (e.g. Microbiology testing) could introduce additional competencies that have not been assessed (e.g. new analytical techniques)
Unlikely to be able to accredit a flexible scope under such broad boundaries
The applied-for flexibility may not be appropriate, either entirely or partly

## Slide 9: Flexible scope
The accredited service is in effect responsible for ‘granting’ accreditation for new tests within the boundaries of the flexible scope
UKAS are responsible for this under fixed scopes
Services must therefore have a management system capable of delivering these additional responsibilities
Awareness of specific accreditation requirements for flexible scopes

## Slide 10: Relevant Publications
UKAS:
GEN 4
European Co-Operation for Accreditation (EA):
EA-2/15M:2019 (requirements for flexible scopes) – currently under revision
EA-4/17M:2022 (scope description for medical laboratories)
International Laboratory Accreditation Co-Operation (ILAC):
ILAC-G18:12/2021 (scope description, mainly)

## Slide 11: Flexible Scope: Key requirements for services
Only applying flexibility within the defined boundaries
Competency to implement new activities (i.e. meet the requirements of ISO 15189)
Assuring the technical/clinical validity of newly introduced activities (as UKAS would for ETS)
Competency for developing, independently reviewing (= ETS assessment) and authorising (= granting accreditation) new activities
Incorporation of flexible scope protocols into the internal audit programme, risk assessment process and management reviews
Informing users whether activities are within the bounds of the flexible scope

## Slide 12: Flexible Scope: Key requirements for services
Documentation of policies & procedures
Maintenance of records sufficient to allow internal audit & external assessment (UKAS and possibly others) to reconstruct the introduction of each new activity to the accredited scope
Inform UKAS periodically of new activities within the flexible scope
Accurate and detailed list of accredited activities, available to UKAS, users and other stakeholders, sufficient to identify what is in the accredited scope at any given time (as Schedules do)

## Slide 13: Schedule of Accreditation
Fixed Scope
Flexible Scope
Refers to:
A flexible scope
Flexible scope protocols
List of analytes within the flexible scope
Sample type(s)
Analyte, determinant etc.
Key equipment & techniques
Location(s)

## Slide 14: Flexible Scope
Analyte, determinant etc. | Date authorised (Issue date)
Sodium | 01/09/2019
Potassium | 06/09/2019
Calcium | 24/09/2019
Creatinine | 15/11/2019
Albumin | 28/11/2019
Ammonia | 25/12/2019
Issue date
The flexible scope Schedule does not show when analytes were ‘granted’ accreditation to be within the flexible scope by the accredited service
Controlled list (referenced on the Schedule) shows this information: